UEFI
Unified Extensible Firmware Interface
© 2013, Mahdi Sadeghi. Licensed under the Creative Commons Attribution 3.0 license, http://creativecommons.org/licenses/by/3.0/

---
HISTORY: BIOS
Basic Input/Output System (BIOS):
Invented by Gary Kildall in 1976 for CP/M OS
Built into the PC
First software run by a PC
Purposes:
Initialize & test hardware components
Run an OS or other program from mass memory
MS-DOS used it for disk, keyboard & text display, others like linux does not rely on BIOS services
Modern BIOSes:
Interactive UI, boot selection, password, and so on.

---
Motivations for a new specification
- To overcome BIOS limitations in mid 1990:
  - 16-bit processor mode:
    - Real mode, also called real address mode, is an operating mode of all x86-compatible CPUs. Real mode is characterized by a 20-bit segmented memory address space
  - 1 MB of addressable space based on IBM 5150 & Intel 8088 design
  - The MBR limits on the number and size of disk partitions (up to 4 primary partitions per disk, up to 2 TiB* (240 bytes = Tebibyte) per disk)
    * Binary prefix for Terabyte (TB) = 1012 bytes

---
What is UEFI
- UEFI is a specification that defines a software interface between an operating system and platform firmware
- Meant to replace BIOS
- Legacy support for BIOS services
- Remote diagnostics and repair of computers without any OS

---
History: UEFI
- Original EFI invented by Intel for it's Itanium systems in mid-1990s
- In 2005, UEFI deprecated EFI 1.10
- UEFI is managed by the Unified EFI Forum
- The current UEFI specification, version 2.3.1, was approved in April 2011.

---
UEFI Features
UEFI variables: provide a way to store data, in particular non-volatile data, that is shared between platform firmware and operating systems or UEFI applications
UEFI provides device-independent time services: include support for timezone & daylight saving
Graphics: rich preboot applications, localized strings, fonts, and forms
EFI shell: to execute other EFI apps

---
UEFI Features cont.
- Extensions: can be loaded from any non-volatile storage. EFI partitions.
- UEFI does not rely on a boot sector
  - Boot variables: path to the loader
  - OS loaders are a class of UEFI applications: e.g. \EFI\BOOT\BOOTx64.EFI
  - Supported file systems include FAT32, FAT16 and FAT12 (accessible by firmware)
- UEFI 2.1 specs:
  - cryptography, network authentication and the User Interface Architecture

---
Features cont.
- UEFI requires the firmware and operating system loader to be size-matched
  - a 64-bit UEFI implementation can only load a 64-bit UEFI OS boot loader
- EFI defines two types of services:
  - Boot services: only when UEFI owns the platform
  - Runtime services: accessible when OS is up
    - Date, Time, NVRAM access
- Compatibility Support Module (CSM): emulates a BIOS environment
- Size-matched: a 64-bit UEFI implementation can only load a 64-bit UEFI OS boot loader

---
Secure Boot
- UEFI 2.2 specification adds a protocol known as secure boot, it can prevents the loading of drivers or OS loaders that are not signed with an acceptable digital signature
- it has 3 modes:
  - Setup mode: to add initial platform key (PK) to firmware
  - User mode: mode after initial setup
  - Custom mode: to add incompatible PKs

---
Advantages over BIOS
- Ability to boot from large disks (over 2 TiB) with a GUID Partition Table, GPT
- CPU-independent architecture
- CPU-independent drivers
- Flexible pre-OS environment, including network capability
- Modular design: extensions

---
Advantages over BIOS cont.
- UEFI understands long mode:
  - allows applications in the pre-boot execution environment to have direct access to all of the memory using 64-bit addressing
- GPT instead of MBR
  - GPT allows for a maximum disk and partition size of 8 ZiB (270 bytes)
  - Linux supports GPT if compiled with CONFIG_EFI_PARTITION
  - Fat32 for sys partitions & Fat12/16 for removable devices.

---
Microsoft & Windows 8
- With the release of Windows 8 in October 2012, Microsoft's certification requirements now require that computers include firmware that implements the UEFI specification.
- If the computer supports the "Connected Standby" feature of Windows 8,	then the firmware is not permitted to contain a Compatibility Support Module (CSM)

---
Installation notes
- If you have preinstalled OS in EFI mode you should install others in EFI mode too
- Use ubuntu 64bit, 32bit versions will not detect EFI
- Support for UEFI SecureBoot appeared in 12.10 and 12.04.2
- With manual partitioning you should create an EFI partition

---
Installation notes cont.
- UEFI-aware OS:
  - the term booted from a (U)EFI means directly booting the system using a (U)EFI OS loader stored on any storage device
  - If you want to disable/enable UEFI you will not be able to boot old installed OSes
- Linux kernel has been able to use EFI at boot time since early 2000
- Grub+Linux also supports booting from a GUID partition table without UEFI
- Ubuntu added support for UEFI secure boot as of version 12.10

---
Ubuntu installation steps
- Ubuntu-Secure-Remix 64bit or of Ubuntu (>=12.04.2) 64bit (contains boot repair tool) or latest release
- Disable QuickBoot/FastBoot and Intel Smart Response Technology (SRT)
  - In case of signature error disable SecureBoot
- Install OS as always
- If OS does not load afterwards use live disk and boot repair to fix boot (recommended repair)
[Speaker Notes: https://help.ubuntu.com/community/UEFI]

---
Boot Repair

---
Criticism: UEFI & Freedom
- EFI as an attempt to remove the ability of the user to truly control the computer
- Secure boot: Boot only signed bootloaders in ARM
- More control for manufacturers and support teams and others?

---
Issues
- In 2012, it was discovered that certain Lenovo computer models with secure boot had firmware that was hard-coded to only allow "Windows Boot Manager" or "Red Hat Enterprise Linux" to load
- In January 2013, a bug surrounding the UEFI implementation on some Samsung laptops was publicized, which caused them to be bricked after installing a Linux distribution in UEFI mode

---
Which one is better?
For me BIOS still is enough
Manufacturers think UEFI is better for them

---
References
http://en.wikipedia.org/wiki/Unified_Extensible_Firmware_Interface
http://www.uefi.org/home/
https://help.ubuntu.com/community/UEFI
https://help.ubuntu.com/community/UEFIBooting
http://mjg59.dreamwidth.org/22855.html

---
Any questions?
Thank you